## Slide 1: Markov Chain for Slotted Aloha
CSMA

## Slide 2: 1. Markov Chain for Slotted Aloha
Slotted Aloha
Time is divided into slots of one packet transmission period
If a node has packet to send => it waits until the start of the next slot to send it.
If have only one node send packet during a slot, the transmission is successful. Otherwise collision
+ Node becomes backlogged node
+ Each backlogged node waits for random time before retransmiting

## Slide 3: Slotted Aloha
Assumptions:
-Single receive, many transmitters
-Poisson arrival rate λ
-Transmitters send broadcast
to notify about their choice
-Receiver immediately feedback
+Idle (0)
+Success (1)
+Collision (e)

## Slide 4: Markov Chain for Slotted Aloha
m: total number of nodes
n: number of backlogged nodes at the beginning of a given slot
Each state represents for number of backlogged nodes
Have (m+1) states (from 0 backlogged node to m backlogged nodes)
-Find the probability of successful transmission of each node in each timeslot by Markov Chain

## Slide 5: Markov Chain for Slotted Aloha
+ Find steady-state probabilites π =(,,…, ,
( Steady-state probability when system is on state i)
+ With each state will find a probability of successful transmission T
With (m+1) state will have …
Probability of successful transmission of each node in each timeslot:
P =

## Slide 6: Find steady-state vector π
A backlogged node transmits in each slot with probability until successful
A unbacklogged node transmits in each slot with probability
: The probability have є backlogged nodes transmit
: The probability have є unbacklogged nodes transmit
=
= ..

## Slide 7: Markov Chain for Slotted Aloha
The state transition probability from state to state +)
P(+)=

## Slide 8: A stationary state distribution must satisfy the condition
π=P.π
And => Find stationary stare
-With (m,n) : state of n backlogged nodes (0 ≤ n ≤ m)
G(n) : Attempt rate as the expected number attempt transmission in a slot in state : G(n) = (m-n).qa + n.qr
: Probability of successful transmission of each node in each time slot:

## Slide 9: Throughput is probability of successful transmission in a slot

## Slide 10: CSMA
-Nodes listen to the channel before they start transmission
Channel idles => Transmit
Channel busy => Wait (join backlog)

## Slide 11: Transmission Options
+ 1 persistent + Non persistent
Channel
Channel idle
Channel busy
Transmit
Nodes sense
Channel
Channel idle
Transmit
Channel busy
Wait random time
Nodes sense

## Slide 12: 1- persistent
.

## Slide 13: Transmission Options
P-persistent
Nodes sense
Channel
Channel idles
Probability to transmit?
Transmit/ ≤P
Wait next slot/ ≥ P
Sense Channel
Random time to sense/ channel busy
Channel busy
Wait next slot
Channel idle

## Slide 14: CSMA/CD
If a node is transmitting it will monitor for collision during the transmission by comparing transmitted data with received data
Start
Nodes sense channel
Send data/ channel idle
Detect collision?
Transmit successful/No collision
Stop transmission/ detect collision
Set random time to wait
Wait time

## Slide 15: CSMA/CD
Time to wait when collision occur:
: Number of time to wait: = random(0,
Time to wait before start again .

## Slide 16: CSMA/CA
.
Start
Nodes sense channel
Channel Idle
Send RTS
Receive CTS?
Transmit successfully/ Received CTS
Set ramdom time to wait
Wait time

## Slide 17: CSMA/CA
Prevent collision before they happen
A spectrum divided into N bands
Assume that RTS messages have the same time duration for all users
When have idle period before transmitting, randomly chooses one band over the N to send a permission request message (RTS) to the destination node
It waits for receiving an authorization message (CTS) from the destination node before transmitting data
=> Collision can occur with RTS => wait random time and start again